## Slide 1: KiCad PCB 设计讲座
以NFC名片设计为例
清华大学未来通信兴趣团队
张庭梁

## Slide 2: Part 1 PCB及电子电路相关知识补充

## Slide 3: Part 2 设计
Copyright © ZHANG TINGLIANG 2019

## Slide 4: ISO 7810
ISO 7810，是身份证、银行卡等尺寸的国际标准，分为ID-1、ID-2、ID-3及ID-000四种。现时采纳的版本为2003年版。
样式 | 尺寸 | 用途
ID-1 | 85.60 × 53.98 mm | 绝大多数银行卡及身份证
ID-2 | 105 × 74 mm | 法国身份证等；签证
ID-3 | 125 × 88 mm | 护照
ID-000 | 25 × 15 mm | SIM卡
ID-1的规定尺寸为85.60×53.98毫米（3.370×2.125英寸），常用于身份证、银行卡（如提款卡、信用卡）、驾照、个人名片，以及商店发出的忠实顾客卡等。
其长宽比与黄金分割（1.618:1）接近。
ISO 7813规范ID-1塑胶银行卡的附加特性，包括0.76毫米厚度，及3.18毫米半径的圆角。

## Slide 5
设计为
85.60×53.98毫米
3.18毫米半径的圆角
0.76毫米厚度（做0.8mmPCB板）

## Slide 6: 丝印和Top图案设计和导入
使用Ai设计表面丝印BMP

## Slide 8: Referance
https://en.wikipedia.org/wiki/ISO/IEC_7810

## Slide 9: NFC原理和天线设计
https://www.themobileknowledge.com/wp-content/uploads/2018/07/02-Webinar-slies-Antenna-design-for-NTAG-I2C-plus.pdf

## Slide 10: 下面是补充知识，不想听电路的同学可以先睡一会

## Slide 11: How NTAG I2C plus works
2

## Slide 12: NFC focus products for each application need
3
Readers/connected tags: for embedded electronics
NFC Frontend solutions
NFC reader with NFC Reader SW Library
NFC controller solutions
NFC reader with integrated
32-bit Cortex MCU and either integrated
firmware or freely programmable memory
Connected tag solutions
NFC tags with non-volatile memory and host connection or integrated MCU
All round
High-perf multi-protocol reader
CLRC663 plus
Entry level
Specialist
Features and price
Plug&Play NFC for Linux, Android,
WinIoT
PN7150
One chip system, programmable NFC controller with DPC
PN7462 family
High-perf full NFC with DPC
PN5180
Proximity&vicinity readers
MFRC630
(ISO14443A – Reader for NTAG® and MIFARE® product families)
SLRC610
(ISO15693 / ISO18000-3M3 - Reader for ICODE® family)
NTAG I²C plus
Single-chip MCU with integrated NFC tag
LPC8N04

## Slide 13: How NTAG I2C plus works
4
Field Detection
Energy harvesting
SRAM memory
SRAM mirroring
Pass-through mode
Memory access management
Originality signature
The NTAG I²C plus connects to the microcontroller via the I²C serial bus interface
NFC-enabled mobile device connects to the MCU via the NFC interface, using the I²C as the communication conduit
The NTAG I²C plus needs to be connected to the antenna coil with LA and LB pads

## Slide 14: NTAG I2C plus support package: Antenna design files
5
SW3641 - NTAG I2C plus
flex antenna Class 6
SW3639 - NTAG I2C plus Class 4
AN11276 – NTAG Antenna design
guide
NXP offers the designs files for the Class 4 and Class 6 antennas included as part of the NTAG I2C plus Explorer kit (OM5569)
If you do not have constrains about the antenna size or shape:
If you need your custom antenna for your design:
NXP offers an Excel-based coil calculation tool to estimate the inductance of rectangular and round antennas *
* More details in slide 18

## Slide 15: Basic antenna theory for NTAG I2C plus tags
6

## Slide 16: NTAG I2C plus electrical input capacitance
7
NTAG I2C plus IC
FD
Vout
SCL
SDA
Gnd VCC
to MCU
NTAG I2C plus equivalent circuit
CIC= NTAG I2C plus input capacitance (50pF)
La
Lb
NTAG I2C plus IC connections
La, Lb = NTAG I2C plus pads to be connected to the antenna
It is the most important factor for the
antenna design.
The form factor and the parameters of the antenna are affected by the input capacitance
NTAG I2C plus IC input capacitance
Antenna coil

## Slide 17: Antenna coil electrical equivalent circuit
8
NTAG I2C plus IC
FD
Vout SCL
SDA
Gnd VCC
to MCU
NTAG I2C plus equivalent circuit
CIC= NTAG I2C plus input capacitance (50pF)
La
Lb
Antenna coil
A
n t e
n
na
c o
i l
Antenna coil
Antenna coil equivalent circuit
Each antenna is a resonant circuit with a specific input impedance.
This input impedance is complex and consists of an inductance, capacitance as well as some losses represented by a resistance.
The actual values depend on
Antenna material
Thickness of conductor
Distance between the windings
Number of turns
Shielding layer
Environment

## Slide 19: Antenna design procedure for NTAG I2C plus tags
11

## Slide 20: Antenna design procedure for NTAG I2C plus tags
12
The precision of the antenna equivalent inductance computation, the length of the connection between the chip and its antenna, and the environment (metal surface, ferromagnetic material) impact the tuning frequency.
1. Design the antenna coil
Determine the size and the specs of the antenna
(number of turns, track width, spacing, etc.)
2. Measure antenna coil
Characterize R,L,C antenna coil parameters
3. Calculate the resonant capacitor value Determine the value of resonant capacitor to set the tag to the target resonant frequency
4. Assemble & measure resonant frequency Measure the resonant frequency and adjust the capacitor value if needed
Antenna coil
NTAG I2C plus + antenna coil= resonance circuit
NTAG I2C plus |  | Connection / Assembly |  | Resonant capacitor |  | 

## Slide 21: Design the antenna coil
13

## Slide 22: Antenna class based on ISO/IEC14443
14
ISO/IEC 14443-1 defines 6 antenna classes, also referred to in ISO/IEC 15693.
The use of ISO/IEC14443 antenna class is optional but it has been established that the use of a prescribed class may enhance interoperability

## Slide 23: Antenna parameters for rectangular and round antennas
15
Inductance of an antenna depends on the antenna dimensions and material properties
Antenna geometry
a0 → Definition of the overall length (mm)
b0 → Definition of the overall width (mm)
w → Track width in mm
g → Gap between tracks (mm)
t → Track thickness
N → Number of turns
Antenna geometry
D0 → | Definition of the antenna diameter (mm) | •
w → g → t → N → | Track width in mm, Gap between tracks (mm), Track thickness Number of turns | •
Material properties
ρ → Electric conductivity εr → Permittivity of card material

## Slide 24: Coil design calculation sheet
Excel calculation sheet tool included in https://www.nxp.com/docs/en/application-note/AN11276.zip
16
This coil design guide calculation sheet uses antenna dimensions and estimates the antenna equivalent inductance.
The following steps are a reliable method to design and fine tune a custom antenna coil:
  Estimation of the electrical parameters
  Definition of the target inductance
  Definition of the dimensions
  Definition of the matrix run
  Production of samples
  Selection of the best coil parameters
  Definition of second matrix run (if needed)

## Slide 25: Measure the antenna coil parameters
17

## Slide 26: Measuring the antenna coil parameters
18
The antenna loop has to be connected to a network analyzer to measure the antenna equivalent circuit (Ra, La, Ca)
Before each measurement, the network analyzer must
be calibrated (open, short and load compensation).
  Settings: S11
  Chart: Smith Z
  Start frequency: 1 MHz
  Stop frequency: Above self-resonant frequency
Note: The antenna has to be at the final mounting position to consider all parasitic effects like metal influence on quality factor, inductance and additional capacitance
High-end or Low-end network analyzer (e.g., miniVNA PRO)
Fig. Antenna series equivalent circuit (Ca, La, Ra)
NTAG I2C plus
Antenna coil

## Slide 27: Calculate the resonant capacitor value
19

## Slide 28: Calculating the parallel resonance capacitor
20
NTAG I2C plus IC
A
n t e
n
na
c o
i l
Antenna coil
Rcon Ccon
Rcon
Connection
La
Lb
Antenna coil
𝐶
𝑓𝑟 − 𝑐𝑢𝑟𝑟𝑒𝑛𝑡
=
1
2 · 𝜋 · 𝑓
𝑟𝑒𝑠
2 · 𝐿
We measure the current system resonance frequency (𝑓𝑟 − 𝑐𝑢𝑟𝑟𝑒𝑛𝑡) after connecting the NTAG I2C plus to the antenna coil.
If it is not 𝑓𝑟 − 𝑐𝑢𝑟𝑟𝑒𝑛𝑡~ 13.56𝑀𝐻𝑧 , we calculate the system capacitance at the current resonance frequency with this formula:
Note: The inductance of the system is basically the inductance of the antenna (L=La).

## Slide 29
21
Calculating the parallel resonance capacitor (II)
If we fix the desired system resonance frequency (𝑓𝑟 − 𝑡𝑎𝑟𝑔𝑒𝑡), the capacitance required so that the system resonates at that target frequency can be calculated with this formula:
NTAG I2C plus IC
A
n t e
n
na
c o
i l
Antenna coil
Rcon Ccon
Rcon
Connection
La
Lb
Tag
CRes
Resonance capacitor
𝑡𝑎𝑟𝑔𝑒𝑡
𝐶 =
1
2 · 𝜋 · 𝑓𝑟
−
2 · 𝐿
𝑡𝑎𝑟𝑔𝑒𝑡
We can calculate the extra capacitance that needs to be soldered in parallel (CRes) by:
𝐶𝑅𝑒𝑠 = 𝐶𝑡𝑎𝑟𝑔𝑒𝑡 − 𝐶𝑓𝑟 − 𝑐𝑢𝑟𝑟𝑒𝑛𝑡
Note: For single tag operation, a tuning slightly above 13.56 MHz would lead to maximum read-/write distance. Due to manufacturing tolerances, a nominal frequency of 14.5 MHz for single tag operation is recommended.
Antenna coil
Resonance capacitor

## Slide 30: Assemble & measure resonant frequency
22

## Slide 31: Assembling and measuring the tag resonant frequency
23
Assemble the calculated 𝑪𝒓𝒆𝒔 capacitor in your design.
Then, measure the resonant frequency (𝒇𝒓𝒆𝒔) at which the resistance impedance (Z) is maximum
If the resonant frequency is not the target resonant frequency, fine tune the capacitor value. If the frequency is high, increase the capacitor value; if low, decrease it.
Resonance Antenna coil
capacitor
Fig. Example of a tag adjusted to 𝒇𝒓𝒆𝒔 = 13.564 MHz

## Slide 32: Recap and closure
29

## Slide 33: Recap of the antenna tuning steps followed
30
Design the antenna coil
Determine the size and the specs of the antenna
(number of turns, track width, spacing, etc.)
Measure antenna coil
Characterize R,L,C antenna coil parameters
Calculate the resonant capacitor value Determine the value of resonant capacitor to set the tag to the target resonant frequency
Assemble & measure resonant frequency Measure the resonant frequency and adjust the capacitor value if needed
We selected 54x27mm PCB antenna board included in OM5569-NT322E kit
We separate the NTAG I2C plus from the PCB board to characterize the antenna parameters
We solder an extra capacitance of 100pF
This is the adjusted antenna tuning at
𝒇𝒓𝒆𝒔 =13.8MHz

## Slide 34: Further information
31
NTAG I2C plus:
http://www.nxp.com/products/:NT3H2111_2211
NTAG antenna design guide: https://www.nxp.com/docs/en/application- note/AN11276.zip
Get your technical NFC questions answered: https://community.nxp.com/community/identificati on-security/nfc
List of Approved Engineering Consultants (AEC) for NFC:
https://nxp.surl.ms/NFC_AEC

## Slide 35: Altium Designer PCB Design
清华大学未来通信兴趣团队
张庭梁

## Slide 36: Part 3 AD20使用
Copyright © ZHANG TINGLIANG 2020

## Slide 37: Part 4 PCB交付制作和元件焊接
张庭梁

## Slide 38: PCB代工厂
嘉立创
国外：https://jlcpcb.com/
国内：https://www.sz-jlc.com/
捷多邦
国外：https://www.pcbway.com/
国内：https://www.jdbpcb.com/

## Slide 41: 元件购买
立创商城
https://www.szlcsc.com/

## Slide 44: 贴片焊接
锡膏+热风枪+精密镊子
电烙铁
SMD Soldering Microscope Footage
https://www.youtube.com/watch?v=tQHDSXDZYF4

## Slide 45: QFN封装
SOP封装的芯片和引脚间距都较大的QFP，基本上直接用刀头加锡往外刮两下就完事，问题不大。这里重点讲下引脚密集的QFN封装的焊接。先固定芯片，步骤如下：
• 把芯片平置于 PCB 上，焊盘不用加锡，否则芯片放不平，极易虚焊
• 注意芯片一脚方向与PCB对应（一脚通常在小圆圈或正看丝印左下角位置）
• 对齐芯片四边引脚与焊盘，要兼顾四边是个非常虐心工作
• 烙铁加锡固定的一边的边缘几个引脚，查看四边对齐情况，没对准还有挽救机会——用烙铁重新调整芯片位置
• 烙铁加锡固定对边的几个引脚

## Slide 46
这样一来芯片就被固定好了，接下来就开始焊了（很多元件都是“先固定，再焊接”的套路），焊的时候也需留个心眼：
1、选择没有焊锡固定的一边，开始焊接
2、用烙铁蘸助焊剂涂抹一边引脚与焊盘
3、从一边加锡，拼命加到形成锡球
4、用烙铁往另一边引流焊锡，被锡润湿过的引脚自然就焊上了
5、用烙铁头的粘性把多余的锡移除。
6、如法炮制剩下的三边
7、四边都焊好后检查引脚是否黏连、短路，必要时补焊。

## Slide 47
总之焊芯片只要记住两点： 1、焊的时候先多加锡，引脚连起来也无所谓，焊好后再慢慢分开。 2、多加助焊剂，助焊剂能让焊锡流动性更好，而不是像一坨粘粘的shi一样。油管上有个视频专教焊QFP芯片的：Professional SMT Soldering: Hand Soldering Techniques - Surface Mount。

## Slide 48: 电容电阻、二极管
电容电阻等二端元件是最常见的了，比较常用的焊法是：先给一边焊盘上锡，用镊子焊上一边固定，再焊另一边。这种方法最大的好处就是易于调整元件位置（因为有镊子辅助），所以焊好的元件看起来整齐美观。缺点也很明显——效率太低（也是因为要拿镊子）。尤其在面对有大量元件的PCB时，一个一个脚的焊似乎有点慢……

## Slide 49: Ref
http://mcu.eetrend.com/blog/2017/100008018.html

## Slide 50: Part 5 写入信息

## Slide 51: 使用NFC App即可
NFC Tools/ NFC Tools Pro
https://play.google.com/store/apps/details?id=com.wakdev.wdnfc&hl=zh

## Slide 54: 绿板子上的效果

## Slide 62: Tips
U? R? J?编号 Tools-Annotation-Annotate Schematics Quietly
Shift+Space键切换走线方式